## Slide 1
Statics of a Particle

## Slide 2: Introduction
This chapter builds on chapter 3 and focuses on objects in equilibrium, ie) On the point of moving but actually remaining stationary
As in chapter 3 it involves resolving forces in different directions
Statics is important in engineering for calculating whether structures are stable

## Slide 3
Teachings for
Exercise 4A

## Slide 4: Statics of a Particle
You can solve problems involving particles in equilibrium by considering forces acting horizontally and vertically
Similar to chapter 3, for these types of problem you should:
Draw a diagram and label the forces
Resolve into horizontal/vertical or parallel/perpendicular components
Set the sums equal to 0 (as the objects are in equilibrium, the forces acting in opposite directions must cancel out…
Solve the equations to find the unknown forces…
4A
y
x
4N
P N
Q N
30°
45°
4Sin45
4Cos45
PCos30
PSin30
The particle to the left is in equilibrium. Calculate the magnitude of the forces P and Q.
 This means the horizontal and vertical forces cancel out (acceleration = 0 in both directions so F = 0)
Choose a direction as positive and sub in values
Rearrange
Divide by Cos30
Resolve Horizontally
Calculate

## Slide 5: Statics of a Particle
You can solve problems involving particles in equilibrium by considering forces acting horizontally and vertically
Similar to chapter 3, for these types of problem you should:
Draw a diagram and label the forces
Resolve into horizontal/vertical or parallel/perpendicular components
Set the sums equal to 0 (as the objects are in equilibrium, the forces acting in opposite directions must cancel out…
Solve the equations to find the unknown forces…
4A
y
x
4N
P N
Q N
30°
45°
4Sin45
4Cos45
PCos30
PSin30
The particle to the left is in equilibrium. Calculate the magnitude of the forces P and Q.
 This means the horizontal and vertical forces cancel out (acceleration = 0 in both directions so F = 0)
Choose a direction as positive and sub in values
Add Q
Calculate Q using the exact value of P from the first part
Resolve Vertically
P = 3.27N
You will usually need to identify which direction is solvable first, then solve the second direction after!

## Slide 6: Statics of a Particle
You can solve problems involving particles in equilibrium by considering forces acting horizontally and vertically
The diagram to the right shows a particle in equilibrium under a number of forces.
Calculate the magnitudes of the forces P and Q
 Start by resolving in both directions
4A
y
x
Q N
P N
1N
2N
40°
55°
PSin40
QSin55
QCos55
PCos40
Choose a direction as positive and sub in values
Resolve Horizontally
Choose a direction as positive and sub in values
Resolve Vertically
Simplify
1)
2)

## Slide 7: Statics of a Particle
You can solve problems involving particles in equilibrium by considering forces acting horizontally and vertically
The diagram to the right shows a particle in equilibrium under a number of forces.
Calculate the magnitudes of the forces P and Q
Start by resolving in both directions
You can now solve these by rearranging one and subbing it into the other!
Q = 0.769N
4A
y
x
Q N
P N
1N
2N
40°
55°
PSin40
QSin55
QCos55
PCos40
1)
2)
2)
Replace P with the Q equivalent
Multiply all terms by Cos40
Add Cos40
Factorise Q on the left side
Divide by the bracket
Calculate

## Slide 8: Statics of a Particle
You can solve problems involving particles in equilibrium by considering forces acting horizontally and vertically
The diagram to the right shows a particle in equilibrium under a number of forces.
Calculate the magnitudes of the forces P and Q
Start by resolving in both directions
You can now solve these by rearranging one and subbing it into the other!
Q = 0.769N
P = 0.576N
4A
y
x
Q N
P N
1N
2N
40°
55°
PSin40
QSin55
QCos55
PCos40
1)
2)
1)
Sub in Q (use the exact value)
Calculate

## Slide 9: Statics of a Particle
You can solve problems involving particles in equilibrium by considering forces acting horizontally and vertically
The diagram shows a particle in equilibrium on an inclined plane under the effect of the forces shown.
Find the magnitude of the force P and the size of angle θ.
 Start by splitting forces into parallel and perpendicular directions
4A
2N
PN
8N
5N
θ
30°
30°
PCosθ
PSinθ
5Cos30
5Sin30
Resolving Parallel
Resolving Perpendicular
1)
2)
Use P as the positive direction and sub in values
Rearrange to leave PCosθ
Use P as the positive direction and sub in values
Rearrange to leave PSinθ

## Slide 10: Statics of a Particle
You can solve problems involving particles in equilibrium by considering forces acting horizontally and vertically
The diagram shows a particle in equilibrium on an inclined plane under the effect of the forces shown.
Find the magnitude of the force P and the size of angle θ.
 Start by splitting forces into parallel and perpendicular directions
4A
2N
PN
8N
5N
θ
30°
30°
PCosθ
PSinθ
5Cos30
5Sin30
1)
2)
1)
2)
Divide equation 2 by equation 1
Each side must be divided as a whole, not individual parts
P’s cancel, Sin/Cos = Tan
Work out the fraction
Use inverse Tan

## Slide 11: Statics of a Particle
You can solve problems involving particles in equilibrium by considering forces acting horizontally and vertically
The diagram shows a particle in equilibrium on an inclined plane under the effect of the forces shown.
Find the magnitude of the force P and the size of angle θ.
 Start by splitting forces into parallel and perpendicular directions
4A
2N
PN
8N
5N
θ
30°
30°
PCosθ
PSinθ
5Cos30
5Sin30
1)
2)
1)
Divide by Cosθ
Sub in the exact value for θ
Calculate P

## Slide 12
Teachings for
Exercise 4B

## Slide 13: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A particle of mass 3kg is held in equilibrium by two light inextensible strings. One of the strings is horizontal, and the other is inclined at 45° to the horizontal, as shown. The tension in the horizontal string is P and in the other string is Q.
Find the values of P and Q.
4B
P
Q
3g
QCos45
QSin45
45°
Resolve vertically
Choosing Q as the positive direction, sub in values…
Add 3g
Divide by Sin45
Calculate

## Slide 14: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A particle of mass 3kg is held in equilibrium by two light inextensible strings. One of the strings is horizontal, and the other is inclined at 45° to the horizontal, as shown. The tension in the horizontal string is P and in the other string is Q.
Find the values of P and Q.
4B
P
Q
3g
QCos45
QSin45
45°
Resolve horizontally
Choosing Q as the positive direction, sub in values…
Add P
Sub in the value of Q from before
Calculate P

## Slide 15: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A smooth bead, Y, is threaded on a light inextensible string. The ends of the string are attached to two fixed points X and Z on the same horizontal level. The bead is held in equilibrium by a horizontal force of 8N acting in the direction ZX. Bead Y hangs vertically below X and angle XZY = 30°.
Find:
The tension in the string
The weight of the bead
4B
X
Z
Y
30°
mg
8
30°
T
T
Draw a diagram
Since this is only one string and it is inextensible, the tension in it will be the same
Call the mass m, since we do not know it…
TCos30
TSin30
Resolve Horizontally
Sub in values, choosing T as the positive direction
Add 8
Divide by Cos30
Calculate

## Slide 16: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A smooth bead, Y, is threaded on a light inextensible string. The ends of the string are attached to two fixed points X and Z on the same horizontal level. The bead is held in equilibrium by a horizontal force of 8N acting in the direction ZX. Bead Y hangs vertically below X and angle XZY = 30°.
Find:
The tension in the string
The weight of the bead
4B
X
Z
Y
30°
mg
8
30°
T
T
Draw a diagram
Since this is only one string and it is inextensible, the tension in it will be the same
Call the mass m, since we do not know it…
TCos30
TSin30
Resolve Vertically
Sub in values, choosing T as the positive direction
Add mg
Sub in the value of T
This is all we need!
The question asked for the weight, not the mass! (weight being mass x gravity…)
Be careful on this type of question. If particle is held by 2 different strings, the tensions may be different in each!

## Slide 17: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A small bag of mass 10kg is attached at C to the ends of two light inextensible strings AC and BC. The other ends of the strings are attached to fixed points A and B on the same horizontal line. The bag hangs in equilibrium with AC and BC inclined to the horizontal at 30° and 60° respectively as shown.
Calculate:
The tension in AC
The tension in BC
4B
A
B
10g
C
30°
60°
T1
T2
T1Cos30
T1Sin30
T2Cos60
T2Sin60
Resolving Horizontally
Sub in values, choosing T2 as the positive direction
Add T1Cos30
Divide by Cos60
Draw a diagram
 The strings are separate so use T1 and T2 as the tensions

## Slide 18: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A small bag of mass 10kg is attached at C to the ends of two light inextensible strings AC and BC. The other ends of the strings are attached to fixed points A and B on the same horizontal line. The bag hangs in equilibrium with AC and BC inclined to the horizontal at 30° and 60° respectively as shown.
Calculate:
The tension in AC
The tension in BC
4B
A
B
10g
C
30°
60°
T1
T2
T1Cos30
T1Sin30
T2Cos60
T2Sin60
Resolving Vertically
Draw a diagram
 The strings are separate so use T1 and T2 as the tensions
Sub in values, choosing T2 as the positive direction
Replace T2 with the expression involving T1
Multiply all terms by Cos60
Add 10gCos60 and factorise left side
Divide by the bracket
Calculate!

## Slide 19: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A small bag of mass 10kg is attached at C to the ends of two light inextensible strings AC and BC. The other ends of the strings are attached to fixed points A and B on the same horizontal line. The bag hangs in equilibrium with AC and BC inclined to the horizontal at 30° and 60° respectively as shown.
Calculate:
The tension in AC
The tension in BC
4B
A
B
10g
C
30°
60°
T1
T2
T1Cos30
T1Sin30
T2Cos60
T2Sin60
Find T2 by using the original equation…
Draw a diagram
 The strings are separate so use T1 and T2 as the tensions
Sub in the value of T1
Calculate!

## Slide 20: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A mass of 3kg rests on the surface of a smooth plane inclined at an angle of 45° to the horizontal. The mass is attached to a cable which passes up the plane and passes over a smooth pulley at the top. The cable carries a mass of 1kg which hangs freely at the other end. There is a force of PN acting horizontally on the 3kg mass and the system is in equilibrium.
By modelling the cable as a light inextensible string and the masses as particles, calculate:
The magnitude of P
The normal reaction between the mass and the plane
4B
45˚
45˚
45˚
R
T
T
1g
3g
3gCos45
3gSin45
PCos45
P
PSin45
Find the tension using the 1kg mass
Resolve in the direction of T and sub in values
Add 1g
9.8N
9.8N

## Slide 21: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A mass of 3kg rests on the surface of a smooth plane inclined at an angle of 45° to the horizontal. The mass is attached to a cable which passes up the plane and passes over a smooth pulley at the top. The cable carries a mass of 1kg which hangs freely at the other end. There is a force of PN acting horizontally on the 3kg mass and the system is in equilibrium.
By modelling the cable as a light inextensible string and the masses as particles, calculate:
The magnitude of P
The normal reaction between the mass and the plane
4B
45˚
45˚
45˚
R
1g
3g
3gCos45
3gSin45
PCos45
P
PSin45
Resolve Parallel to find P
9.8N
9.8N
Choose P as the positive direction and sub in values
Rearrange
Divide by Cos45
Calculate

## Slide 22: Statics of a Particle
You need to know when to include additional forces on your diagrams, such as weight, tension, thrust, the normal reaction and friction
A mass of 3kg rests on the surface of a smooth plane inclined at an angle of 45° to the horizontal. The mass is attached to a cable which passes up the plane and passes over a smooth pulley at the top. The cable carries a mass of 1kg which hangs freely at the other end. There is a force of PN acting horizontally on the 3kg mass and the system is in equilibrium.
By modelling the cable as a light inextensible string and the masses as particles, calculate:
The magnitude of P
The normal reaction between the mass and the plane
4B
45˚
45˚
45˚
R
1g
3g
3gCos45
3gSin45
PCos45
P
PSin45
Resolve Perpendicular to find R
9.8N
9.8N
Choose R as the positive direction and sub in values
Rearrange
Calculate

## Slide 23
Teachings for
Exercise 4C

## Slide 24: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
We have seen before that FMAX is the maximum frictional force possible between two surfaces, and that it will resist any force up to this amount
Remember that the frictional force can be lower than this and still prevent movement
In statics, FMAX is reached when a body is in limiting equilibrium, ie) on the point of moving
It is important to consider which direction the object is about to move as this affects the direction the friction is acting…
4C
A block of mass 3kg rests on a rough horizontal plane. The coefficient of friction between the block and the plane is 0.4. When a horizontal force PN is applied to the block, the block remains in equilibrium.
Find the value for P for which the equilibrium is limiting
Find the value of F when P = 8N
R
3g
3kg
P
F
Resolve vertically for R
Sub in values with R as positive
Add 3g
Find FMAX
Sub in values
Calculate
For part b), if P = 8N then equilibrium is not limiting, and P will be matched by a frictional force of 8N
3g
So if P = 11.76N, then the block is in limiting equilibrium on the point of moving

## Slide 25: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A mass of 8kg rests on a rough horizontal plane. The mass may be modelled as a particle, and the coefficient of friction between the mass and the plane is 0.5.
Find the magnitude of the maximum force PN, which acts on this mass without causing it to move if P acts at an angle of 60° above the horizontal.
4C
8g
8kg
P
F
R
60°
PCos60
PSin60
Draw a diagram
 Find the normal reaction as we need this for FMAX
Resolve Vertically
Find FMAX
Sub in values with R as positive
Rearrange to find R in terms of P
Sub in values
Multiply bracket out

## Slide 26: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A mass of 8kg rests on a rough horizontal plane. The mass may be modelled as a particle, and the coefficient of friction between the mass and the plane is 0.5.
Find the magnitude of the maximum force PN, which acts on this mass without causing it to move if P acts at an angle of 60° above the horizontal.
4C
8g
8kg
P
F
R
60°
PCos60
PSin60
Draw a diagram
 Find the normal reaction as we need this for FMAX
Resolve Horizontally
Sub in values with P as positive
 The horizontal forces will cancel out as the block is in limiting equilibrium
Sub in FMAX
‘Multiply out’ the bracket
Add 4g
Factorise P on the left side
Divide by the bracket
Calculate
If P is any greater, the block will start to accelerate.
If P is any smaller, then FMAX will be less and hence the block will not be in limiting equilibrium

## Slide 27: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A box of mass 10kg rests in limiting equilibrium on a rough plane inclined at 20° above the horizontal. Find the coefficient of friction between the box and the plane.
Draw a diagram
We need to find FMAX so begin by calculating the normal reaction
4C
20
20
10g
10gCos20
10gSin20
R
F
Resolving Perpendicular
Finding FMAX
Sub in values with R as positive
Rearrange
Sub in R and leave µ

## Slide 28: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A box of mass 10kg rests in limiting equilibrium on a rough plane inclined at 20° above the horizontal. Find the coefficient of friction between the box and the plane.
Draw a diagram
We need to find FMAX so begin by calculating the normal reaction
Now you can resolve Parallel to find µ
4C
20
20
10g
10gCos20
10gSin20
R
F
Resolving Parallel
Sub in values with ‘down the plane’ as positive
Sub in FMAX
Add µ(10gCos20)
Divide by the bracket
Calculate

## Slide 29: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A parcel of mass 2kg is placed on a rough plane inclined at an angle θ to the horizontal where Sinθ = 5/13. The coefficient of friction is 1/3. Find the magnitude of force PN, acting up the plane, that causes the parcel to be in limiting equilibrium and on the point of:
Moving up the plane
Moving down the plane
4C
Find the other trig ratios – this will be useful later!
Opp
Hyp
Adj
5
13
12
θ
So the opposite side is 5 and the hypotenuse is 13
Use Pythagoras to find the missing side!
Now you can work out the other 2 trig ratio…

## Slide 30: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A parcel of mass 2kg is placed on a rough plane inclined at an angle θ to the horizontal where Sinθ = 5/13. The coefficient of friction is 1/3. Find the magnitude of force PN, acting up the plane, that causes the parcel to be in limiting equilibrium and on the point of:
Moving up the plane
Moving down the plane
4C
θ
R
2g
θ
2gCosθ
2gSinθ
P
F
Start with a diagram
P is acting up the plane, on the point of causing the box to move
Friction is opposing this movement
Resolving Perpendicular for R
Sub in values with R as the positive direction
Finding FMAX
Rearrange
Sub in values
Remove the bracket

## Slide 31: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A parcel of mass 2kg is placed on a rough plane inclined at an angle θ to the horizontal where Sinθ = 5/13. The coefficient of friction is 1/3. Find the magnitude of force PN, acting up the plane, that causes the parcel to be in limiting equilibrium and on the point of:
Moving up the plane
Moving down the plane
4C
θ
R
2g
θ
2gCosθ
2gSinθ
P
F
Start with a diagram
P is acting up the plane, on the point of causing the box to move
Friction is opposing this movement
Resolving Parallel for P
Sub in values with P as the positive direction
Sub in F
Rearrange for P
Sub in Sinθ and Cosθ
Calculate

## Slide 32: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A parcel of mass 2kg is placed on a rough plane inclined at an angle θ to the horizontal where Sinθ = 5/13. The coefficient of friction is 1/3. Find the magnitude of force PN, acting up the plane, that causes the parcel to be in limiting equilibrium and on the point of:
Moving up the plane
Moving down the plane
4C
θ
R
2g
θ
2gCosθ
2gSinθ
P
F
We now need to adjust the diagram for part b)
Now, as the particle is on the point of sliding down the plane, the friction will act up the plane instead…
FMAX will be the same as before as we haven’t changed any vertical components
F
Resolving Parallel for P
Sub in values with P as the positive direction
Replace F
Rearrange
Sub in Sinθ and Cosθ
Calculate

## Slide 33: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A parcel of mass 2kg is placed on a rough plane inclined at an angle θ to the horizontal where Sinθ = 5/13. The coefficient of friction is 1/3. Find the magnitude of force PN, acting up the plane, that causes the parcel to be in limiting equilibrium and on the point of:
Moving up the plane
Moving down the plane
4C
θ
R
2g
θ
2gCosθ
2gSinθ
P
We now need to adjust the diagram for part b)
Now, as the particle is on the point of sliding down the plane, the friction will act up the plane instead…
FMAX will be the same as before as we haven’t changed any vertical components
F
A force of 13.57N up the plane is enough to bring the parcel to the point of moving in that direction. Any more will overcome the combination of gravity and friction and the parcel will start moving up
A force of 1.51N up the plane is enough, when combined with friction, to prevent the parcel from slipping down the plane and hold it in place. Any less and the parcel will start moving down.

## Slide 34: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A box of mass 1.6kg is placed on a rough plane, inclined at 45° to the horizontal. The box is held in equilibrium by a light inextensible string, which makes an angle of 15° with the plane. When the tension in the string is 15N, the box is in limiting equilibrium and about to move up the plane.
Find the value of the coefficient of friction between the box and the plane.
4C
45°
1.6g
1.6gSin45
1.6gCos45
R
15°
15N
15Cos15
15Sin15
F
Draw a diagram – ensure you include all forces and their components in the correct directions
 The box is on the point of moving up, so friction is acting down the plane
 Find the normal reaction and use it to find FMAX
Resolving Perpendicular
Sub in values with R as the positive direction
Finding FMAX
Rearrange
Sub in values
45°

## Slide 35: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A box of mass 1.6kg is placed on a rough plane, inclined at 45° to the horizontal. The box is held in equilibrium by a light inextensible string, which makes an angle of 15° with the plane. When the tension in the string is 15N, the box is in limiting equilibrium and about to move up the plane.
Find the value of the coefficient of friction between the box and the plane.
4C
45°
1.6g
1.6gSin45
1.6gCos45
R
15°
15N
15Cos15
15Sin15
F
Draw a diagram – ensure you include all forces and their components in the correct directions
 Now resolve parallel to create an equation you can solve for μ.
45°
Resolving Parallel
Sub in values with ‘up’ the plane as the positive direction
Replace F
Add μ term
Divide by the bracket
Calculate!

## Slide 36: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A box of mass 1.6kg is placed on a rough plane, inclined at 45° to the horizontal. The box is held in equilibrium by a light inextensible string, which makes an angle of 15° with the plane. When the tension in the string is 15N, the box is in limiting equilibrium and about to move up the plane.
Find the value of the coefficient of friction between the box and the plane.
 The tension is reduced to 10N. Determine the magnitude and direction of the frictional force in this case
4C
45°
1.6g
1.6gSin45
1.6gCos45
R
15°
15N
15Cos15
15Sin15
F
Update the diagram (or re-draw it!)
 Calculate the new FMAX, first finding the new R…
45°
10N
10Sin15
10Cos15
Resolving Perpendicular
Sub in values with R as the positive direction
Finding FMAX
Rearrange
Sub in values
Calculate

## Slide 37: Statics of a Particle
You can also solve statics problems by using the relationship F = µR
A box of mass 1.6kg is placed on a rough plane, inclined at 45° to the horizontal. The box is held in equilibrium by a light inextensible string, which makes an angle of 15° with the plane. When the tension in the string is 15N, the box is in limiting equilibrium and about to move up the plane.
Find the value of the coefficient of friction between the box and the plane.
 The tension is reduced to 10N. Determine the magnitude and direction of the frictional force in this case
4C
45°
1.6g
1.6gSin45
1.6gCos45
R
15°
F
Update the diagram (or re-draw it!)
 Calculate the new FMAX, first finding the new R…
45°
10N
10Sin15
10Cos15
 Add up the forces acting parallel to the plane (ignoring friction for now)
Resolving Parallel (without friction)
The force up the plane will be given by:
As this is negative, then without friction, there is an overall force of 1.428N acting down the plane
Therefore, friction will oppose this by acting up the plane
As FMAX = 4.012N, the box will not move and is not in limiting equilibrium

## Slide 38: Summary
We have learnt about resolving forces when a particle is in limiting equilibrium
We have seen when and how to include additional forces such as tension and friction
We have looked at situations where friction acts in different directions